## JSQ-2000D/C/E-S

4 Digit Dual Display Single Timer Relay Control Instrument

JSQ-2000D/C/E-SS

## 4 Digit Dual Display Dual Timer Relay Control Instrument

JSQ-2000D-L

8 Digit Dual Display Single Timer Relay Control Instrument

JSQ-2000E            JSQ-2000C              JSQ-2000D

1. General Description:

The JSQ-2000D/C/E timers are used to control relay with programmable delay time. The start of delay can either be triggered by pressing a key on the front panel or by pulling an input terminal to low. The delay can also be pulsed by pressing a key or shorting an input terminal to ground. The shorting method is especially useful when the device is used with other micro controller devices.

Dual Display: upper display shows running delay time, lower display shows the programmed total delay time.

2. Specification:

- Power supply: 90-240VAC

- Power consumption: less than 3w

- Max relay control output: AC: 220V 3A, DC: 24V 5A (resistive load)

- Relay control life: 100,000 times

- Operating temperature: 0 – 40 oC

- Storage temperature: -20 -- +60 oC

3. Models:

| Type | Model number | Max delay time | Note |
| --- | --- | --- | --- |
| Single Timer Delay | JSQ-2000C/D/E-S-1 | 0.01 –99.99 second | Count down |
|  | JSQ-2000C/D/E-S-2 | 1 –9999 second | Count down |
|  | JSQ-2000C/D/E-S-3 | 1 sec – 99min59sec | Count down |
|  | JSQ-2000C/D/E-S-4 | 1min – 99hr59min | Count down |
|  | JSQ-2000C/D/E-S-5 | 1min – 9999min | Count down |
|  | JSQ-2000C/D/E-S-6 | 0.01 –99.99 second | Count up |
|  | JSQ-2000C/D/E-S-7 | 1 –9999 second | Count up |
|  | JSQ-2000C/D/E-S-8 | 1 sec – 99min59sec | Count up |
|  | JSQ-2000C/D/E-S-9 | 1min – 99hr59min | Count up |
|  | JSQ-2000C/D/E-S-10 | 1min – 9999min | Count up |
| Dual Timer Delay | JSQ-2000C/D/E-SS-1 | 1 –9999 second | Count down |
|  | JSQ-2000C/D/E-SS-2 | 1 sec – 99min59sec | Count down |
|  | JSQ-2000C/D/E-SS-3 | 1min – 9999min | Count down |
|  | JSQ-2000C/D/E-SS-4 | 1min – 99hr59min | Count down |
|  | JSQ-2000C/D/E-SS-5 | 1 –9999 second | Count up |
|  | JSQ-2000C/D/E-SS-6 | 1 sec – 99min59sec | Count up |
|  | JSQ-2000C/D/E-SS-7 | 1min – 9999min | Count up |
|  | JSQ-2000C/D/E-SS-8 | 1min – 99hr59min | Count up |
| 8 digit** single large delay timer | JSQ-2000C/D/E -L-1 | 0-99hr59min59.99sec | 8 sec reset* |
|  | JSQ-2000C/D/E -L-2 | 0-9999hr59min59sec | 8 sec reset |
|  | JSQ-2000C/D/E -L-3 | 0-9999day23hr59min | 8 sec reset |
|  | JSQ-2000C/D/E -L-4 | 0-99hr59min59.99sec | Instant reset+ |
|  | JSQ-2000C/D/E -L-5 | 0-9999hr59min59sec | Instant reset |
|  | JSQ-2000C/D/E -L-6 | 0-9999day23hr59min | Instant reset |

*    need to hold down the reset button for 8 seconds to reset

**  during normal operation, 8 digit displays the running counter.  Press ▲ key  to show the programmed max delay time.

+   Instant reset when press the reset button

4. Relay control types:

When timer expires, relay close or open.