# MB1000 Volt/Ampere Digital Panel Meter

General Description:

The MB1000 digital panel meters are used to display various physical measurements such as AC/DC current and voltage. The meter uses 0.8 inch large LED display.

Sepcification:

- 3 and half 0.8 inch large LED display (+/- 1999);

- user can set the decimal point location

- AC power supply 90-240V

- Operating temperature: -10 to 50 oC

- Calibrated at 25 oC

Models:

| Model | Input range | Accuracy |
| --- | --- | --- |
| MB1000A | 0~100mA | +/- 0.5% |
| MB1000B | 0~2A | +/- 0.5% |
| MB1000C | 0~5A | +/- 0.5% |
| MB1000D | 0~10A | +/- 0.5% |
| MB1000E | 0~100A | +/- 0.5% |
| MB1000F | 0~2V | +/- 0.5% |
| MB1000G | 0~20V | +/- 0.5% |
| MB1000H | 0~50V | +/- 0.5% |
| MB1000I | 0~150V | +/- 0.5% |
| MB1000J | 0~250V | +/- 0.5% |
| MB1000K | 0~400V | +/- 0.5% |
| MB1000L | 0~500V | +/- 0.5% |

Connection Terminals:

Terminals 7 and 8 are AC power input. Terminals 1 and 2 are input signal. Terminal 1 is positive and terminal 2 is negative.